## Slide 1: Oligonucleotide Synthesis Manufacturing Facility Project Enabling Technology for the Present and the Future
ISPE-CASA 2018 Technology Conference
March 13, 2018
Sheron Branham Associate Director ASO Process Engineering
Paul Richards Principal Engineer Global Process Engineering

## Slide 2: Topics of discussion
Antisense oligonucleotides (aso)
Project Overview
Process Overview
Challenges and Solutions
Results

## Slide 3
Speakers
  Paul Richards
  Principal, Global Process Engineering
        BS Chemical Engineering – UConn
        MS Management – Rensselaer
        30 years experience – API, OSD, Fine Chemical
        5 years at Biogen
  Sheron Branham
  Associate Director, ASO Process Eng & Mfg
        BS Chemical Engineering from Clemson University
        Expected MBA from NC State in May!
        19 years in Pharmaceutical Mfg – API and OSD
        5 years at Biogen

## Slide 4
Clinical Manufacturing (as needed)
Milestone and Royalty Payments
Knowledge Transfer
Regulatory
Manufacturing
Commercialization
Development through Registration
Drug Discovery

## Slide 5
ALS
Alzheimer’s
Parkinson’s
SMA
Biogen’s Therapeutic Focus for ASOs

## Slide 6
What is an Antisense Oligonucleotide?

## Slide 7
What is an Antisense Oligonucleotide?

## Slide 8
Benefits:
Same equipment and raw materials used for all molecules
Reduced development time
Rapid tech transfer and startup
Minimizes cost of implementation
Speed to patient
Spinraza Sequence
G
2’ MOE
MeU
2’ MOE
A
2’ MOE
MeC
2’ MOE
MeC
2’ MOE
MeU
2’ MOE
MeU
2’ MOE
MeU
2’ MOE
MeC
2’ MOE
A
2’ MOE
MeU
2’ MOE
A
2’ MOE
A
2’ MOE
MeU
2’ MOE
G
2’ MOE
MeC
2’ MOE
MeU
2’ MOE
G
2’ MOE
5’
3’
A True “Platform” Process
Notes: Building blocks . Unlike small molecule – unique chemistry and process for each – expensive

## Slide 9
Raw Materials
(nucleotide building blocks)
grow chemically on a resin bead
G
G
MeU
…
…one unit at a time…
MeU
MeU
AEX Purification
Detritylation
& Neutralization
HIC Purification
Automated Solid-Phase Synthesis
Ready-to-fill
Product
UF/DF
Novel Biologics-like Aqueous Purification
3 Rxn/ Cycle Synthesis
Ammonolysis / Cleavage
ASO Manufacturing Process

## Slide 10
Chart: ASO Total Demand (No. of Batches)
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027
Clinical | 3.8519 | 8.3752 | 11.8664 | 11.9727 | 14.6442 | 16.7086 | 18.6667 | 17.7407 | 18.6667 | 19.5926
Commercial | 0 | 0 | 1 | 1 | 1 | 1 | 2 | 3 | 7 | 27
Biogen’s Projected Demand for ASOs

## Slide 11
1970:
ASO chemistry first described
1996:
Major advancement in ASO chemistry
1998:
First ASO Approved by FDA
2012:
40 ASOs in Clinical Trials
2013-2017:
Four more ASOs approved by FDA
2018:
147 ASOs in Clinical Trials
347% increase in # molecules!
Oligonucleotide Industry
First Blockbuster!
Notes: Development began in 1970s
1996 – major advancements in ASO chemistry
First FDA Approval of an ASO (Vitravene) in 1998
40 molecules in clinical trials in 2012
Second FDA Approval of an ASO (Kynamro) in 2013
Two approved (Spinraza and Exondys 51) in 2016
Macugen(aptamer) Eteplirsen, vitravene
147 molecules in clinical trials right now

## Slide 12
Ask again in 18 months
Ok, but we need 18 months notice and a large non-refundable reservation fee.
Supplier 1
Supplier 2
Supplier 3
Three CMOs asked to bid…

## Slide 13
Growing ASO pipeline
High Cost to Outsource
Build $19 M
ASO Facility
Supply Risk Mitigation
Limited CMO Capacity
Limited Flexibility and Significant Lead Time with CMO
But… With Zero Headcount Change
Decision to Build

## Slide 14
Build technical capability and capacity
Provide pivotal clinical supply
Deliver commercial materials
Plant operations
Global reach
Manufacturing and Support staff
Lab space
Scientists
Build cGMP Facility
Develop - Stage 1
Manufacture -Stage 2
Extend- Stage 3
Trigger: Commercial product and multiple clinical programs
Trigger: Second commercial
product in phase 3 trials and commercial platform defined
Phased Approach to Investment

## Slide 15
Warehouse space to GMP manufacturing in 16 months
Project Goals
Renovate a warehouse and build a new cGMP ASO facility
Deliver product to the clinic on time
Create flexible, efficient, and scalable systems and equipment to support the future pipeline
A Mission to Reach the Clinic

## Slide 16
>2000 Liters Solvent / kg product
Facility Design Overview
Notes: Safety first?

## Slide 17
Facility Overview |  |  |  | 
Scope cGMP oligonucleotide synthesis manufacturing facility to support clinical and commercial production Renovation of high bay warehouse and packaging area ~ 5,000 ft2 first floor ~ 1,000 ft2 mezzanine |  |  |  | 
Synthesis Scale - 0.5 – 3.3 kg/batch (final product) |  |  |  | 
 | Synthesis Scale | Implementation | Final Product | Synthesis Column
 | 163 mmol | Year 1 | ~ 0.5 kg | 30 cm
 | 367 mmol | Year 1 | ~ 1.0 kg | 45 cm
 | 1000 mmol | TBD | ~ 3.3 kg | 75 cm
Expansion Capability – facility and equipment designed to facilitate adding a second synthesizer train |  |  |  | 
Facility Capabilities
Notes: Update table – remove solvent purification
Consider bookending scale options
More pics in general

## Slide 18
Unique Challenges
Notes: ASOs are chemically synthesized. Current products are biologics (grown from cells in an aqueous process) and small molecule drug product (formulation and powder handling). Chemistry expertise only in technical development who supports external API manufacturing for small molecules. Started organization from this group –
Challenges: high solvent usage, flammable/toxic materials; evolving demand/facility needs for next 10 years; no experience in ASOs; flexible thinking – particularly with QA requirements

## Slide 19
EHS
Consultants
Facility Design
ASO Experienced engineering firm
Operations
Chemical mfg experience
Process Engineering
Organic Chemistry
Learning Agility
Questioning attitude
Ionis Site Visits
Safety-conscious
Ionis team
Systems approach
Hands-on
Generalists
Involve Tech Dev in design
External
Internal
Challenge 1: Skilled Resources Closing the Gaps in Expertise
Notes: What else to add to facility design?

## Slide 20
Expert mentors: Ionis & technical development scientists
Attended live batch run at Ionis
Seamless knowledge transfer from Ionis
Practice Time: water runs, solvent runs, engineering batch
Hands-on training at Cambridge Pilot Plant
Challenge 1: Skilled Resources Manufacturing Staff Readiness

## Slide 21
        General Protection
        Walk-in Fume Hoods
        High Air Change rates
        Control Room to minimize time staff is on the floor
  Flammables
    Hazardous Area Electrical Classification
    Electrostatic dissipative flooring
    Active monitoring of grounding and bonding
    Corrosives
    Higher Alloys
    Spill containment below grade
  Toxic /Odorous
    Ventilated Weigh/Dispense enclosure
    Closed charging
    Minimize raw material sampling / Tailgate samples
  Fire Water Containment Pit
    30 minutes fire water containment per code
    Process spill containment tank within pit
Challenge 2: Elevated Safety Risk Engineering Controls
Notes: Replace pics with new pit pic, make pics really big

## Slide 22
  Equipment / Process Design
        Nitrogen Inertion – automatic purge cycles and nitrogen blanketing
        Powder Prep hood for solid weighing (amidites / PADS)
        Closed process transfers
        Closed sampling for Deblock
        Active monitoring of grounding and bonding of equipment
        Emergency vent knock out tank
        Recycletainers for solvents / reagents (return & refill)
      Keyed connections for raw materials
      High purity, closed system supplied with N2 blanket
        Bulk organic waste tank and collection system
        Carbon absorption system for process vents
Challenge 2: Elevated Safety Risk Engineering Controls

## Slide 23
CHALLENGE
Closed processing where practical
    Reduce risk of operator exposure to hazardous materials
    Reduce risk of fire
    Downgrade hazardous area electrical classification (Div 1 -> Div 2)
SOLUTION
Recycletainers
    Safety and quality
    Closed transfers
    Bubble traps/ day tanks
Separate Weigh/Dispense for powder handling
2 areas of open processing
    Small volume flammable weigh/dispense in hood in Weigh Room
    Large volume open processing for synthesis column packing and cleaning within fume hood
Challenge 2: Elevated Safety Risk Engineering Controls: Process Closure

## Slide 24
Transition from Fear to Confidence
Go/No Go Meetings
New Safety Tools / Systems
Expert Confirmation
Practice Opportunities / Small Wins
Constant Reinforcement
Challenge 2: Elevated Safety Risk Cultural Considerations
Notes: Communications to management – opportunities to verbalize/vet out concerns. Constant reminders on importance. Clarity in expectations for behavior. New tools to enable open assessment/conversations.
From Fear to Confidence
No blame environment

## Slide 25
CHALLENGE
Capacity
    Support clinical and commercial pipeline based on drug portfolio forecast
SOLUTION
Space planning
    Solvent delivery Tote manifolds for pre-made solutions
    Expandable Synthesis suite for 2nd Synthesizer and Ammonolysis Hood
    Ample mezzanine space for Solution vessels to feed synthesizer skids
    Pipe Bridge, Area for 2 future bulk tanks outside
Future Build-out
Current Facility Design
Challenge 3: Evolving ASO Pipeline Flexibility for Expansion

## Slide 26
CHALLENGE
Design to allow for future infrequent downstream processing
    Vacuum Stripping in Ammonolysis Operation
    HPLC with Methanol/water/acetate
    Ethanol Precipitations
    Acid Detritylation
    Lyophilization
SOLUTION
HVAC
    Capacity designed in to process as ISO 8 in Synthesis suite
    ISO 7 Processing in Lyophilizer Room
Space allocated, and process utility drops provided, for Downstream Processing
    Equipment procurement deferred
    Install shell space for lyophilization room and associated airlocks.
Challenge 3: Evolving ASO Pipeline Flexibility for Purification

## Slide 27
Material Safety Stock
Scalable Staffing Model
Templated & Flexible Documents
Reduced Tech Transfer Time
Challenge 3: Evolving ASO Pipeline System Flexibility
Notes: Templated Documents, Formula, material inventory safety stock, scalable staffing model

## Slide 28
Raw materials only available from the “chemical industry”
Biogen’s quality systems designed for Biologics
Solution:
Supplier Audits
Technical Risk Assessments
Additional Quality Testing
Procedural updates
Challenge 4: Quality Systems Raw Material Sourcing
Notes: Challenge with sourcing from the chemical industry – use in a pharmaceutical environment / systems. Had to get around requirements – justify not following procedures with technical assessments, quick procedural changes, or additional controls. Example of supplier – lack of quality systems had to add extra testing to ensure confidence, another similar issue, wrote up justification of why material was non-critical.

## Slide 29
CHALLENGE
Prevent Mix-up
  Raw Materials - How to confirm correct totes are hooked up to correct charging station?
  Amidite Solutions - How to confirm correct amidites are charged to correct synthesizer inlet port?
  Nitrogen versus Air
SOLUTION
Engineering Controls
  Different keyed Swagelok QTM fittings on recycletainers for each solvent / reagent
  Synthesizer design to facilitate installation of PAT for on-line amidite ID confirmation
    Prevent incorrect coupling sequence
  Swagelok quick disconnects for N2
  Staubli quick disconnects for compressed air
Challenge 4: Quality Systems Engineering Controls

## Slide 30
16 months later…

## Slide 31
Higher yield than comparison batches
Comparable impurity profiles
Biogen process scaled up smoothly
Results
Chart: Purity (%)
Ionis | 86.1672
Pilot Average | 89.88
Engineering run | 86.9338
GMP Run | 90.32
Chart: Yield (%)
50.1 | 50.1
Pilot Average | 67.0394
Engineering run | 68.5746
GMP Run | 71.7342
Notes: Update from alex

## Slide 32
Construction of $19 M ASO synthesis facility
Procurement and Qualification of 51 equipment systems and 251 instruments
Sourcing, procurement, and release of 24 new raw materials
Creation or modification of 93 procedures and batch records
Development and/or qualification of 39 analytical methods
Successful production of our first ASO molecule:
On schedule No safety incidents High purity High yield
Full Funding Approval 30Jun16  First GMP Batch 01Nov17
What did we accomplish in 16 months?
Notes: How many materials, procedures, and equipment adds in FVM?? Other topics?

## Slide 33
Thoughtful incremental investments minimize financial risk
Unique challenges arise when implementing novel technologies to existing facilities
Challenge assumptions to find optimal solutions
Oligonucleotides are a growing field with lots of potential
Finding creative options to closing expertise gaps is essential
Summary

## Slide 34
Questions?