## Slide 1: Changing development & manufacturing paradigms in lyophilization through application of predictive process modeling
Jamie Sigmon
Suresh Nulu
ISPE CaSA Technology Conference · March 13, 2018

## Slide 2
Intro to lyophilization
Paradigm shift: current state vs. new state
Mathematical basis for process modeling
Experimental heat transfer studies
Application and verification of the modeling tool
Cross-functional collaboration
Q&A
Overview

## Slide 3
Drug product process overview

## Slide 4
Why lyophilize?
Product A Before and After Lyophilization
Biogen RTP Optimization Cycles
Advantages to lyophilization:
Extend shelf life
Increased flexibility
(eg. reconstitution volume, concentration)
Minimize cold chain
Lyophilization is used to remove liquid from a formulation at low temperatures through the process of sublimation

## Slide 5
Lyophilization basic principle
Freezing
2. Sublimation
The freeze drying process involves freezing a product and then placing under a vacuum, allowing the ice to change directly from solid to vapor without passing through a liquid phase
Under atmospheric pressure, ice converts to liquid (melting) when temperature increases
Under low pressure, ice converts to gas when temperature increases
Notes: Phase diagram of water

## Slide 6
Lyophilization Process Overview
1
2
3
      Freezing and Annealing
      Primary Drying
      Secondary Drying
      Freezing
      Sublimation
      Desorption
      Stochastic in nature
      Physics well understood
      Physics well understood
Primary drying is the longest step in a lyophilization process. Since the physics are well understood, we can apply modeling to enhance process knowledge and improve efficiency.
Notes: Primary drying longest portion of the lyo process. Bulk of moisture is removed here.
Physics are well understood so apply model to better understand and improve efficiency
Other models for secondary drying and sometimes annealing/freezing. We will not discuss these here.

## Slide 7
The Scale-Up Challenge
Total Shelf Area: ~ 4.6ft2 (0.43m2)
Capacity: ~ 500 10R vials
Total Shelf Area: ~ 86ft2 (8m2)
Capacity: ~ 13000 10R vials
Freeze dryers differ quite a bit between scales,
both in capacity and design
19X
Development Scale
Commercial Scale at Biogen DP Site
Notes: Lab scale is the size of a normal home refrigerator.
Compare to manufacturing scale – about the size of a small meeting room.

## Slide 8
Current Development Paradigm:
Process understanding is achieved by collecting data at all scales using experiments
Notes: Trial and error at scale – expensive and time consuming
At a CMO –
Time, scheduling, materials, protocols, data collection, analytical testing, etc.
Could cost upwards of $500,000 for a single development run at scale

## Slide 9
New Paradigm:
Leverage predictive models to minimize/eliminate experiments “at-scale”
1
Comprehensive Development
Small Scale
Pilot Scale
At Scale (Predictive Models)
PVR
“At – Scale”
Increased Predictive Capability
Increased Process Understanding
Increased Assurance of At-scale Parameters
No “At-Scale” Development =
2
3
At Site Verification
?
Scale- Up
Predictive Models
Notes: More process understanding
Savings of time, money
Use high fidelity predictive models in lieu of experiments
Need high confidence in models to replace experiments
Most predictive and accurate models are 1st principle models
Derive from heat/mass transfer equations for sublimation

## Slide 10
High level primary drying
(frozen liquid)
Sublimation
Heat IN
Mass (vapor) OUT
Frozen vials loaded on the shelf of a lyophilizer are subjected to heat transfer such that water vapor escapes via sublimation
Closed system  Heat in = Mass out
Notes: Two important parameters:
-Heat transferred in
-Mass out

## Slide 11
Physics of Primary Drying:
The basis for a mathematical model
Sublimation Physics
(frozen liquid)
Sublimation
Heat IN
Mass (vapor) OUT
=
Container + Equipment
dependent
Formulation + Freezing Profile
dependent

## Slide 12
Four important parameters are used to model the performance of a freeze dryer
Heat Transfer Coefficient
Mass Transfer Coefficient
Freeze Dryer Limitations
Maximum Sublimation Rate
Minimum Controllable Pressure

## Slide 13: Heat Transfer Coefficient (Kv)

## Slide 14
Heat is transferred from the shelf to the vial by three different modes
qcont + qgas
A “total heat transfer coefficient” (Kv) is used to combine all heat transfer into the vials
Contact Conduction
Radiation
= .
Gas Conduction
Notes: = free molecular heat conductivity of gas at 0 C.
= Energy accommodation coefficient
= Effective Distance – characterizing gap between shelf and vial bottom
= heat conductivity of gas at constant pressure
= Surface emissivity of material
= stefan boltzmann constant
𝛿_0 = free molecular heat conductivity of gas at 0 C.
𝛼 = Energy accommodation coefficient
𝑙_𝑣 = Effective Distance – characterizing gap between shelf and vial bottom
𝜑_0= heat conductivity of gas at constant pressure
𝜀= Surface emissivity of material
𝜎 = stefan boltzmann constant

## Slide 15: Total Heat Transfer Coefficient (KV) has a strong dependence on Pc
3 data points are needed to fit Kv vs Pc data to the above equation using regression
Notes: Fill volume and shelf temperature were assessed and had little contribution to Kv

## Slide 16
What does this mean for us? Experimental basis
Measured as water loss
Known
Experimentally determined
Development
Manufacturing
Measured with probe
=

## Slide 17
Kv studies were performed on the lab and manufacturing lyophilizers
Experimentally determine Kv for a given Pc (≥ 3 Pc setpoints)
Fit regression to data
Solve for a, b, c

## Slide 18
Heat maps show hot and cold spots on shelf
Edge Effect
Kv(center) / Kv(edge)
Warm
Cool
No data
Experimental
Shelf Layout
Heat Map
Notes: Heat map based on Kv of each location

## Slide 19
Kv has been mapped for all Biogen lyophilizers
=
We can now model processes in all Biogen lyophilizers and predict performance when transferring a process between lyophilizers

## Slide 20
Predictive models are used to assist with scale up between the lab and manufacturing lyophilizers
EXCEL BASED
1st PRINCIPLES MODEL
Eliminates the need for expensive “at-scale” experiments during development

## Slide 21: From Lab to Manufacturing with full Design Space Understanding in 30 mins

## Slide 22
Product A: Model verification in lab lyophilizer
Model predicted Tp matches thermocouple measured Tp
Model predicted drying time equals experimentally determined time
Model predicted Rp comparable to MTM calculated Rp
Notes: 3 Data Types:
Model
Thermocouple
Experimental (MTM)

## Slide 23
Product B: Model verification in manufacturing lyo
Model predicted Tp matches probe measured Tp (steady state)
Model predicted drying time aligns with end of primary drying

## Slide 24
Our road to success
was built on clarity, unity & agility
Clear Roles & Responsibilities
Unified Goals With INTENT
Agile Team Dynamics
PREPARATION
+

## Slide 25
An Extremely Collaborative & Cross-Functional Team Effort
TD
Manufacturing
MS
Maintenance

## Slide 26
Suresh Nulu
Mehak Mehta
Cherie Parkhurst
Soham Bhatt
Josh Briggs
Chris Shirley
Mark Lee
Benjamin Young
Wendy Hinton
Cassandra Williams
Augustine Mbella
Sheridan Dickens
Robert Archer
Sam Black
David Coley
Daouda Faye
Sean Goudy
Kevin Maloney
Nicole Onyeneho
Stuart Wang
Acknowledgements

## Slide 27
References
Costantino, H., & Pikal, M. (2005). Lyophilization of Biopharmaceuticals (pp. 75-110). AAPS Press.
Pikal, M., Roy, M., & Shah, S. (1984). Mass and heat transfer in vial freeze-drying of pharmaceuticals: role of the vial. J Pharm Sci, 73(9), 1224-37.
Tchessalov, S (ND). Heat and Mass Transfer during Lyophilization: Generation of Inputs for the Primary Drying Model. Breckenridge BPOG Workshop.
Tchessalov, S., Dassu, D., Latshaw II, D., & Nulu, S. (2017). An Industry Perspective on the Application of Modeling to Lyophilization Process Scale up and Transfer. American Pharmaceutical Review. Retrieved 23 May 2017, from http://www.americanpharmaceuticalreview.com/Featured- Articles/335416-An-Industry-Perspective-on-the-Application-of-Modeling-to-Lyophilization- Process-Scale-up-and-Transfer/

## Slide 28
Questions?

## Slide 29: Backup Slides

## Slide 30: Primary Drying Mathematical Model: High Level Logic
Heat In Mass Out
Solve Numerically by Changing Tp
= +
Pi - predicted by mass & heat transfer balance
=
Pi - predicted by vapor pressure equilibrium

## Slide 31: Heat Transfer into vials through direct contact Conduction from shelf
Tchessalov, S (ND)

## Slide 32: Heat Transfer into vials through direct contact Conduction from shelf
Tchessalov, S (ND)

## Slide 33: Heat Transfer into vials by Radiation from walls and shelves
Tchessalov, S (ND)

## Slide 34: Heat Transfer into vials through Gas Conduction and Convection
Tchessalov, S (ND)