## Slide 1: An Overview of Automation and Qualification
Nate Beekman – Avid Solutions
Justin Cook – Sequence Inc

## Slide 2: What is Process Automation

## Slide 3
Product is developed with potential to address a need
Process is designed (Facility, Equipment, and Utilities) to support the manufacturing of the product
Project planning is conducted to establish an overall strategy of how to go from design to validation
    Validation Plans (incl. CSV Val Plan)
    System Assessments (incl. Risk Assessments, Part 11 Assessments, Vendor Assessments)
    System Boundaries
Where does it all start…

## Slide 4
User Requirements Specification (URS) Developed
    Complex and custom software could see further documents developed such as Functional Requirements Specification (FRS)
Automation Integrator interprets requirements and generates a proposed automation design
    Detailed Design Specification (DDS)
Upon client approval of design, integrator develops the software code
Testing is needed to ensure the code meets all design requirements and intended use.
    FAT, SAT, Commissioning, Qualification
Design, Implement, and Test

## Slide 5
Project Implementation

## Slide 6
Breyer’s Ice Cream is pursuing new type/flavor of ice cream
Breyer’s R&D team develops the new product in the lab environment
They capture their product/process knowledge in a process description which is helpful for A&E firm
Breyer’s does a lot of project planning including developing validation plans, etc.
Facility, Equipment, Utilities designed to meet known process needs for the new ice cream
    Establish a need for automation and then compiling associated requirements
Let’s Make Some Ice Cream

## Slide 7
Per facility layout and flow of the process, Breyers has the raw material holding tanks separated a long distance from the ice cream mixing tanks
They decide to implement a DCS to be able to automate the interaction between the two
<CONTINUE WITH DESCRIBING FULL EXAMPLE of how to automate the ice cream making process – Control sequencing>
Add Picture of P&ID
Example Continued

## Slide 8
    Continuous
    Discrete
    Batch
Automation

## Slide 9
Automation Layers

## Slide 10
    PLC’s
    Programmable Logic Controller
    RTU
    Remote Terminal Unit
    Valves
    Sensors
    Pumps
Automation Layers
I/O

## Slide 11
    SCADA
    Supervisory Control And Data Acquisition
    DCS
    Distributed Control System
    HMI
    Human Machine Interface
    Historian
    Data Collection
    Reporting
Automation Layers
Monitoring and Supervising
Notes: Questions: W

## Slide 12
    MES
    Manufacturing Execution Systems
    Electronic Batch Records (EBR)
    Support System Interfacing
    Learning Management Systems (LMS)
    Equipment Asset Management (EAMS)
    Document Management Systems
    Laboratory Information Management (LIMS)
Automation Layers
Enterprise Systems
Notes: Software Support Interfacing

## Slide 13
Per facility layout and flow of the process, Breyers has the raw material holding tanks separated a long distance from the ice cream mixing tanks
They decide to implement a DCS to be able to automate the interaction between the two
<CONTINUE WITH DESCRIBING FULL EXAMPLE of how to automate the ice cream making process – Control sequencing>
Add Picture of P&ID
Example Continued

## Slide 14
Project Testing

## Slide 15
Once the implementation of the automation software is complete – testing ensues
    Internal Development Testing (DT)
    Software Factory Acceptance Test (SFAT)
    Once the automation software is tested and hardware installation is complete on site – testing continues
    Site Acceptance Test (SAT)
    Commissioning (IOV)
    Qualification (IOQ)
Testing Phase

## Slide 16
Debugging the software
Integrator led effort
Line by Line code review – not as focused on process functionality
Checklist
Offline simulation environment
Development Testing

## Slide 17
Likely 3rd party supported effort (if being leveraged towards qualification)
Predetermined acceptance criteria
Offline simulation environment
Test Cases
    Graphics
    Sequence of Operations
    Alarms
    Interlocks
Software Factory Acceptance Test (SFAT)

## Slide 18
All necessary hardware and network infrastructure installed on manufacturing site
Startup Activities
    Code downloaded on site
    Site network communication checks
    Loop Checks, Loop Calibrations
Site Acceptance Testing
    Vendor Supported
    SFAT testing can be leveraged
Site Acceptance Testing (SAT)

## Slide 19
Client Quality Plan
    Documents created/executed per client procedures
    Involved personnel trained under client’s procedures
    Issues handled per client procedures
Can leverage SFAT and SAT testing
Testing to ensure that all design requirements have been met
Commissioning (IOV)

## Slide 20
Risk Based approach allows for limited redundancy of testing
Focused primarily on critical aspects
    Risk assessments help define these
Can leverage SFAT, SAT, IOV
Testing to ensure intended use is met
Qualification (IOQ)

## Slide 21
Managing issues throughout the test execution effort(s)
Engineering Change Management
    Managing changes/issues outside of test execution
Configuration Management
    Managing software changes throughout the implementation
    Import/Export procedures, Download procedures, etc.
Change & Deviation Management

## Slide 22
Traceability to ensure all requirements were tested
    Trace URS to FRS to DDS to SFAT/SAT/IOV/IOQ
Summarize all acceptance criteria were met
    Summarize any critical issues
Trace Matrix and Summary Report